## Slide 1
SWARMOS
Edge-AI Based Distributed Fleet Coordination for Autonomous Mobile Robots in Smart Warehouses
Master Specification - Problem ID SIH26123 - Bharat Electronics Limited - Robotics and Drones
6
modules, all implemented
570
tests green
0
collisions, 18 paired runs
100 ms
hard tick budget, p95 10 ms

## Slide 2
The problem SIH26123 actually states
What BEL asked for, in their words and then in ours
As published
Warehouses run large AMR fleets. Central schedulers are a single point of failure and a bandwidth bottleneck.
Robots must coordinate at the edge: negotiate right of way, avoid deadlock, survive peer failure and radio loss.
Success criterion 1: zero collisions.
Success criterion 2: at least 20 percent reduction in task completion time versus a stop-and-wait baseline.
What that means technically
No central arbiter in the safety path. Each robot decides using only what it can hear inside a 15 m radio horizon.
Message cost must scale with local density, not fleet size - O(k) per robot per tick, not O(n).
Safety must hold under partial information, stale peers, a lying robot, and a robot that has gone completely deaf.
Every claim must be reproducible on demand, from a seed.
We treat C1 as a hard invariant enforced in code, and C2 as a measurement - reported below exactly as it came out.

## Slide 3
What SWARMOS is
A decentralised coordination stack plus the simulator and control centre needed to prove it
SWARMOS is not a path planner with a dashboard on top. It is a four-layer runtime-assurance architecture in which the safety layer is the smallest, simplest and most heavily tested part of the system.
Each robot runs an autonomous agent: it plans, it bids for tasks in a Contract Net auction, it negotiates corridor reservations with whoever it can hear, and it is overruled by a geometric monitor it cannot argue with.
The simulator is the authoritative world. There is exactly one source of robot state, so the UI, the analytics and the coordination layer can never disagree about where a robot is.
Everything is deterministic from a seed. A run is identified by a trace hash, so any behaviour a judge sees can be replayed exactly, including behaviour under a degraded radio.
24k+
lines of application code
3
adversarial scenarios
15 m
radio horizon, enforced
10 Hz
control rate

## Slide 4
Four architectural laws
Non-negotiable. Every module is written to obey these, and tests enforce them structurally.
 | Law | How it is held
L1 | The simulation is the single authoritative source of robot state | No module keeps a private copy of a pose. UI, analytics and coordination all read the same frame.
L2 | Coordination is the binding safety arbiter; its verdict is final | The planner proposes. The arbiter disposes. The geometric monitor sits beneath both and can stop anyone.
L3 | Machine learning is advisory only, never in the safety path | Enforced by an AST test that fails the build if any coordination module imports app.ml.
L4 | One canonical model per concept | All shared types live in app/coordination/models.py. There is no second definition of a robot state anywhere.
L3 is the one people ask about. We measured our forecaster against a persistence baseline, it lost by roughly 4x, and so it stayed advisory. See the X-05 slide.

## Slide 5
System architecture
Six modules, one direction of authority
M5 Simulation
Authoritative world. Physics, tasks, faults, batteries. 10 Hz.
>
M4 Coordination
Auction, reservations, arbiter, monitor. Binding verdicts.
>
M2 Backend
Starlette. REST control plane, WebSocket data plane.
>
M1 Frontend
Vanilla JS + Canvas control centre. No framework.
M3 ML / Edge-AI
Demand forecasting, anomaly hints. Advisory, fenced out of the safety path.
>
M6 Database / Analytics
SQLite event store, KPI rollups, replay by trace hash.
Authority flows left to right along the top row only. M3 and M6 observe and advise; neither can move a robot.

## Slide 6
Frozen conventions
Agreed once, then never renegotiated - this is why six modules integrate without translation layers
Domain | Convention
Space | Continuous 2-D metres. Aisle pitch 1.0 m, robot radius 0.35 m, so a passing pair needs 0.70 m of the 1.0 m aisle.
Heading | Radians in [0, 2pi), 0 = +X, counter-clockwise positive.
Velocity | Metres per second, always >= 0. Direction lives in the heading, never in the sign of the speed.
Time | Tick rate 10 Hz. 100 ms is a hard budget, not a target.
Identity | Robots R###, tasks T###. Zero-padded so lexical order is numeric order, which is what makes tie-breaks total.
Radio | R_comm 15 m. Heartbeat 10 Hz, suspicion at 200 ms, confirmation at 500 ms.
Safety geometry | HARD_STOP 0.75 m, CONFLICT 0.97 m, CAUTION 1.13 m, max step 0.22 m per tick.
Wire format | Envelope schema_version 1.0. Missing values are rendered as -- and never as 0.

## Slide 7
M5 - Simulation
The authoritative world
Specification
SimEngine(scenario, seed=, policy=, label=) - one object owns the world. step() advances exactly one 100 ms tick.
Three scenarios, all adversarial: rush_50 (fleet 50), narrow_aisle_deadlock (fleet 24), blocked_aisle (fleet 40).
Fault injection at runtime: motor stall, radio silence, battery collapse, sensor drift, rogue behaviour.
KPIs computed in-engine: collisions, near misses, completion times, SLA misses, compute p50/p95/p99, veto counts.
Why it is built this way
Determinism is a feature, not an accident. Every random draw comes from one seeded generator, and iteration is over sorted ids.
That gives a trace hash: the same seed produces the same run bit for bit, so a bug seen once can be reproduced forever.
The engine measures its own compute time each tick, which is how we can state a p95 rather than assert real-time performance.
The physics is deliberately simple. The contribution is the coordination, so the world model stays auditable.
Verified: p95 tick compute 10.14 ms at fleet 50 against a 100 ms budget - about 90 percent headroom.

## Slide 8
M4 - Coordination
The binding arbiter
SIMPLEX RUNTIME ASSURANCE (Sha, 2001)
  A complex, high-performance decision layer is wrapped by a simple, verifiable safety layer that has the last word. The complex layer can be wrong; the system still cannot collide.
THE FOUR STAGES
  1. Contract Net auction assigns tasks by bid, with no auctioneer.
  2. Cooperative A* over a time-indexed reservation table claims corridors ahead of time.
  3. Utility-based right-of-way resolves whatever the reservations did not: remaining path, battery, task priority, yield streak.
  4. A geometric monitor enforces HARD_STOP 0.75 m unconditionally. It does not read the plan, the bid or the model - only positions.
DEADLOCK
  Cycles are detected on the wait-for graph (Coffman conditions, Knapp classification) and broken by the same total order used for tie-breaks, so resolution is deterministic rather than randomised back-off.

## Slide 9
One tick, end to end
What happens in each 100 ms, and who can say no
Sense
Read own pose, hear peers within 15 m. Nothing else is available.
>
Advise
M3 offers a demand forecast. Non-binding.
>
Plan
Auction bid, WHCA* path, reservation requests.
>
Arbitrate
Utility contest, deadlock check, verdict per robot.
>
Monitor
Geometric floor. Can override everything above.
>
Act
Bounded step, max 0.22 m. State published once.
Each stage can only reduce freedom, never increase it. A robot that has been told to stop cannot be un-stopped by a later stage, which is what makes the safety argument short enough to actually check.
The verdict object records which stage bound the decision, so the UI can explain any robot's behaviour in one sentence instead of showing a log.

## Slide 10
M3 - Edge-AI, and the decision not to trust it
X-05: we measured our own model and it lost
Configuration | Model MAE | Persistence MAE | Delta | Verdict
Fleet 8 | 5.344 | 0.667 | -701.6 pct | model far worse
Fleet 50 | 2.308 | 0.415 | -456.0 pct | model far worse
A shadow forecaster ran alongside the live system and was scored against the most boring baseline available - persistence, which simply predicts that the next interval looks like the last one.
It lost by roughly four to seven times. So the forecaster stayed advisory, and we wrote the result down instead of quietly shipping it.
Three tests now enforce that structurally: no coordination module may import app.ml; an advisory can never bind a verdict; and a forecaster that throws on every call cannot stop the simulation.
Recorded in docs/X05_FORECASTER_DECISION.md and enforced by tests/test_ml_fence.py. An honest negative result is cheaper than a demo that fails under questioning.

## Slide 11
M2 - Backend
Control plane and data plane, kept separate on purpose
REST control plane
Raw Starlette with an asynccontextmanager lifespan. No framework magic in the request path.
/api/status - run identity, tick, policy, impairment. Deliberately carries no robot array.
/api/sim/inject - fault injection. /api/sim/control - run, pause, step, reset, seed.
/api/cosim - counterfactual co-simulation: fork the world and run the baseline against the same future.
WebSocket data plane
/ws/fleet - one frame per tick carrying robots, KPIs and events with short keys to keep the frame small.
State lives on exactly one channel. A client cannot assemble a half-REST, half-socket view and see two different worlds.
Frames are versioned by schema_version, so a stale client degrades visibly instead of misrendering.
Verified in-process with starlette.testclient, including websocket_connect, so the contract is a test not a promise.

## Slide 12
M1 - Frontend
Vanilla JS and Canvas. No framework, no component library, no gradients.
Design laws
Three levels of ink on one surface. Saturated colour is reserved for robot STATE and nothing else.
One hero metric at 40 px tabular (tasks per minute), three supporting metrics at 20 px. Not a wall of numbers.
Motion only where it carries meaning: 120 to 200 ms, one 400 ms pulse at conflict birth, then a static ring.
Empty states name the cause and the next action. Degraded states are inline banners, not red toasts.
Engineering
Fixed shell: 68 percent map, 22 percent right rail, 10 percent bottom strip. The map never reflows.
Level of detail: below 0.6 zoom robots render as 4 px dots, which is what holds 50+ robots at 30 fps.
Trails are drawn for the selected robot only. Everything else would be noise at fleet scale.
No fake data, ever. A missing value renders as -- through a single exported constant, so zero always means zero.
Keyboard-first: every demo action has a key binding, because a live demo that depends on clicking a small target is a demo that fails.

## Slide 13
M6 - Database and analytics
Evidence, not logging
Every decision that changed a robot's freedom is persisted as an event: who, when, which stage bound it, and why. The event store is the audit trail for the safety claim.
KPI rollups are computed from the event stream, not from a separate counter, so the number on the dashboard and the number in the report cannot diverge.
A run is keyed by its trace hash. Given the hash, the run can be replayed exactly - the same collisions avoided, in the same order, at the same ticks.
That is what makes the whole system falsifiable. Any judge can name a moment in the demo, and we can reproduce that moment offline.
SQLite
no server, no setup
trace_hash
run identity
append-only
event store
replayable
bit for bit

## Slide 14
Novelty register - graded honestly
We separate what is genuinely new from what is competent engineering, because judges do this anyway
 | Contribution | Grade | Note
N1 | Contract Net task auction | Incremental | Known protocol, applied cleanly.
N2 | Cooperative A* with reservations | Table stakes | Expected of any serious entry.
N3 | Deterministic replay by trace hash | Genuine | Rare in student fleet work, and it is what makes every other claim checkable.
N4 | Deadlock detection and resolution | Incremental | Coffman and Knapp, applied to corridors.
N5 | Simplex runtime assurance | Genuine | A verifiable monitor beneath an unverifiable planner.
N9 | Adversarial robot containment | Genuine | A lying robot is detected, quarantined and routed around. Most BEL-relevant behaviour.
N10 | Counterfactual co-simulation | Genuine | Fork the live world and run the baseline against the same future.
X-01 | Sovereign agent mode | Genuine | A deaf robot tightens its own envelope and keeps working.

## Slide 15
N9 - Adversarial robot containment
The behaviour BEL will care about most
Detect
A robot's declared intent stops matching its observed motion. Declared and observed are compared every tick.
>
Suspect
Its claims are discounted in the utility contest, but it is not yet cut off. Faults look like this too.
>
Quarantine
Confirmed rogue. Its reservations are voided and its messages are dropped at the radio layer.
>
Route around
Peers treat it as a moving obstacle with a widened envelope and keep working.
The important property is that containment is a local decision. There is no central authority to declare a robot rogue, so the mechanism still works when the network is partitioned - which is exactly when you would want it to.
A quarantined robot is drawn in its own colour in the control centre, so the operator sees containment happen rather than reading about it afterwards.

## Slide 16
X-01 - Sovereign agent mode
What a robot does when it can no longer hear anyone
The failure we refused to ignore
Every decentralised scheme assumes the robot can hear somebody. Radio dies. Then the robot has no peers, no reservations it can trust, and no arbiter.
The usual answer is to stop dead. In a warehouse aisle, a stopped robot is itself a hazard and a throughput loss.
So we gave it a third option: keep working, but under an envelope it can guarantee alone.
What sovereign mode actually does
Entered only after 5 consecutive confirmation ticks of silence, so a single dropped frame does not trigger it.
Speed is capped at 0.5 of nominal and the clearance margin widens by 0.35 m - it buys safety with time.
It honours only reservations it already holds, and requests nothing new, because it cannot hear a refusal.
Distinct colour in the control centre and a distinct KPI (robots_sovereign), so degradation is visible, not silent.
This is graceful degradation with a stated envelope rather than a fail-stop - and it is the answer to 'what happens when your network goes down?'

## Slide 17
X-23 / X-24 / X-25 - claims turned into receipts
16 tests whose only job is to make three claims falsifiable
 | Mechanism | What the tests actually pin
X-23 | Failure detection and reservation GC | A SUSPECTED peer does not free its corridor; only a CONFIRMED failure does. A transient outage never reaches collection.
X-24 | Deterministic arbitration | The same encounter always resolves the same way, independent of dict insertion order. A symmetric tie breaks by id and stays broken.
X-25 | Bounded radio, O(k) cost | A failure notice is a local event. Neighbour count tracks density, not fleet size: 8, 32 and 64 robots on the same pitch all give an interior robot exactly 2 neighbours.
The X-25 density test is the one worth showing. It is the difference between a system that scales and a system that merely runs at the size we happened to demo.
During development these tests caught a real mistake: we had guessed the FailureEvent field names. The test was corrected to the production contract, not the other way round.

## Slide 18
Success criteria - measured
C1 is met after we found and fixed two real defects. C2 is not met, and we say so.
9000
ticks per run, 27 paired
7 -> 0
SwarmOS collisions
-19.3 pct
C2 mean, sign negative
20 pct
C2 bar - not met
C1: met on the current code - 27 paired runs, 3 scenarios, 9 seeds, 9000 ticks. It was NOT met a week ago. The 1800-tick run that reported PASS never reached the failure, which first appears at tick 700. Next slide is that story.
C1 is necessary, not differentiating: the stop-and-wait control is collision-free too. What it shows is that negotiation, containment and sovereign fallback did not cost us safety - not that they bought it.
C2: NOT MET. Mean -19.3 percent, 95 percent CI [-36.0, -2.6]. It got worse when we fixed defect 2, which is the right direction: a sound step bound withholds speed the arbiter used to grant.
Two findings matter more than that number. Task supply, not run length, binds - 9000 ticks of blocked_aisle is byte-identical to 1800. And avg_completion_s across arms is survivorship-biased: one seed scored +25.9 percent for us only because we finished 3 tasks to the baseline's 12.
Full record in docs/SUCCESS_CRITERIA_VERIFICATION.md, raw log in reports/criteria_after_envelope_fix.log. Reproduce with tools/verify_criteria_powered.py 9000 9.

## Slide 19
How C1 was actually won
A safety argument only ever checked on short runs is not a safety argument
 | Defect | What it was | Fix and effect
1 | Free waypoint snap | SimRobot.step snapped onto a waypoint within 0.08 m charging neither moved nor budget - free travel every tick. A step cleared with 0.0039 m of margin reached 0.6962 m against a 0.75 m floor. | Snap only when the budget affords it, and charge it. 7 -> 1.
2 | Truncated step envelope | The monitor bounded its own step with project_step on the published intent, which stops at the end of a short path. A 0.0440 m projection made every swept gap read as the standing-still gap, so full speed was granted; the engine moved 0.0540 m into a stationary peer. | Keep the direction, extend the distance to MAX_STEP_M. 1 -> 0.
Both broke one invariant: granting speed_scale f must move a robot at most f * MAX_STEP_M. Once that is false no margin means anything - the arbiter is clearing a segment the engine does not respect.
Defect 2 produced zero step-authority breaches, so the test that catches defect 1 was blind to it. Four tests now pin both, all four failing on the pre-fix code. Suite total: 575 passing.
We report this rather than quietly fixing it: the shape of the failure is the transferable lesson, and a judge who ran the demo past 180 seconds would have found it.

## Slide 20
Verification evidence
What we can show on demand, in under a minute each
Evidence | Where | What it establishes
570 tests, all green | 20 files, 70 s wall clock | The gate. No skips, no xfail hiding a broken contract.
Structural ML fence | tests/test_ml_fence.py | AST-walks the coordination package and fails if app.ml is imported.
Deterministic replay | trace_hash | Same seed, same run, bit for bit - including under an impaired radio.
Compute headroom | p95 10.14 ms / 100 ms | Measured in-engine at fleet 50, not asserted.
Forecaster decision | docs/X05_FORECASTER_DECISION.md | A measured negative result, written down.
Criteria record | docs/SUCCESS_CRITERIA_VERIFICATION.md | Includes the criterion we did not meet.
Reproduce the gate: PYTEST_DISABLE_PLUGIN_AUTOLOAD=1 PYTHONPATH=. python3 -m pytest tests/ -q

## Slide 21
The demo, in six minutes
Rehearsed, keyboard-driven, and every beat backed by a mechanism on the earlier slides
T+ | Beat | What the judge sees
0:00 | Fleet running, 50 robots | Establish that it is real: live tick, live KPIs, one hero metric.
1:00 | Select one robot | Its path, its peers, and the one-sentence reason for its current verdict.
2:00 | Force a corridor conflict | Two robots meet in a 1.0 m aisle. Show the contest, and who yielded and why.
3:00 | Kill a robot's radio | It enters sovereign mode: slower, wider margin, still working. Distinct colour.
4:00 | Turn one robot rogue | Detect, quarantine, route around. The fleet keeps running.
5:00 | Co-simulation split screen | Same future, baseline arm beside ours. Then the replay: same seed, same run.
Every beat is triggered by a key binding. Nothing in the demo depends on clicking a moving target.

## Slide 22
Questions we expect, and the honest answer
Prepared, not improvised
Question | Answer
Is this really decentralised, or is the server the brain? | The server is a viewport. Every binding decision is made inside a robot agent from a 15 m horizon. Kill the socket and the fleet keeps coordinating.
Where is the AI? | Advisory, and measured. It lost to persistence by 4x, so we fenced it out of the safety path and documented why. The intelligence in the safety path is the arbitration, not a model.
Did you hit the 20 percent target? | No. +2.3 percent mean, and the measurement is under-powered at n of 1 to 16 tasks. Here is the table, and here is the run that would settle it.
What happens when the network dies? | Sovereign mode. Speed capped at half, margin widened by 0.35 m, existing reservations only. Visible in the UI and in a KPI.
Would this scale to 500 robots? | Message cost is O(k) in local density, tested at 8, 32 and 64 on the same pitch. Compute p95 is 10 ms of a 100 ms budget at 50. We have not run 500, so we will not claim 500.

## Slide 23
What we claim, and what we do not
The second list is the reason to believe the first
We claim, and can demonstrate
Zero collisions - enforced geometrically and pinned by tests.
Deterministic replay from a seed, via trace hash.
Simplex runtime assurance: a verifiable monitor beneath an unverifiable planner.
Adversarial robot detection, quarantine and route-around.
Sovereign operation after total radio loss, under a stated envelope.
O(k) message cost in local density, not fleet size.
10 ms p95 tick compute against a 100 ms budget at fleet 50.
We do not claim
The 20 percent completion-time reduction. Measured at +2.3 percent, under-powered, and not yet answered.
That our forecaster is good. It is worse than persistence and we published the number.
Operation at 500 robots. Untested, therefore unclaimed.
Hardware validation. This is a simulation-backed software stack, and the physics is deliberately simple.
Novelty for N1, N2, N4 and N6 - those are competent engineering, not contributions.
A judge who asks 'what was your n?' ends a cherry-picked claim in one question. A measured miss with a route to a real answer survives the whole Q and A.

## Slide 24
What comes next
Ordered by what would change a conclusion, not by what is easiest
 | Next step | Why it is next
1 | Re-score C2 on a sound statistic | Equal-completion-count time and tasks_per_min, both immune to the survivorship bias in avg_completion_s. No new simulation needed - the paired runs are already on disk.
2 | Raise task supply until neither arm is idle-limited | Measured: blocked_aisle is exhausted well before 1800 ticks, so longer runs cannot power C2. Until supply binds, no coordination policy can move the number and the scenario is the thing to fix.
3 | Scale study | Fleet 100 and 200 with the same seeds, to confirm the O(k) claim holds where it matters.
4 | Hardware-in-the-loop | Replace the physics with a ROS 2 bridge. The coordination layer already talks only to a state contract, so this is a swap, not a rewrite.
The two items that used to head this list - longer runs, and checking whether task supply binds - are now answered, and the answer killed the first one. Item 4 is cheap precisely because of law L1: one authoritative state source means the world model is replaceable.

## Slide 25
SWARMOS
Summary
A decentralised AMR coordination stack in which the safety layer is the smallest and most tested part of the system, every behaviour is replayable from a seed, and the machine learning is advisory because we measured it and it lost.
Six modules, 24 thousand lines, 570 green tests, zero collisions across 18 paired adversarial runs, and one published criterion miss with a stated route to answering it.
570
tests green
0
collisions
10 ms
p95 of 100 ms
1
criterion openly missed
Problem ID SIH26123 - Bharat Electronics Limited - Robotics and Drones