## Slide 1
SWARMOS
Edge-AI Based Distributed Fleet Coordination for Autonomous Mobile Robots in Smart Warehouses
SIH26123 | Bharat Electronics Limited | Robotics and Drones
6-Member Team Plan | v1 - for team review
Read this, then send me your Section-by-Section status using docs/TEAM_MEMBER_STATUS_PROMPT.md

## Slide 2
The Problem
Why today's warehouse fleets are fragile
Modern warehouses run dozens of Autonomous Mobile Robots in shared aisles
The usual approach is cloud-centric central planning. Three failure modes:
  Latency - every movement decision makes a network round trip
  Wi-Fi dead zones - a robot that cannot reach the server cannot act
  Single point of failure - the server dies, the fleet freezes
What the problem statement demands:
  At least 3 AMRs, decentralized inter-robot messaging
  Dynamic conflict AND deadlock resolution
  Task allocation and rerouting, multi-agent path planning
  Multi-robot simulation and a fleet dashboard
Our answer: decide locally, coordinate peer-to-peer, keep the central server for orchestration and analytics only.

## Slide 3
The Only Two Numbers We Are Judged On
Every task in this plan maps back to one of these
0
inter-robot collisions in all tested scenarios
>= 20%
reduction in total task completion time vs stop-and-wait
Both must come from the real benchmark engine. Never hard-coded.
A measured 14% beats a fabricated 22%, because a fabricated number dies in the Q&A round.
This is why the BENCHMARK HARNESS (M6) is the highest-priority item in the entire project - it is the only thing that can produce the number.
And it is why the 3-ROBOT VERTICAL SLICE comes before any novelty work:
  nothing can be measured until robots actually move end to end.

## Slide 4
What SWARMOS Is
A distributed fleet operating system, not a robot simulator
The simulation represents the physical world. It is not the product.
The coordination intelligence IS the product.
The web application is the operational control centre.
Core capabilities:
  Decentralized peer coordination and local decision making
  Spatio-temporal conflict detection - predict conflicts before overlap
  Spatio-temporal corridor reservations - book space AND time
  Decentralized auction / negotiation for contested space
  Deadlock detection and recovery, heartbeat failure detection
  Battery-aware decisions, congestion and blocked-aisle recovery
  Decision explainability, replay, analytics and benchmarking
Demo target: 50 AMRs, with 100+ stress testing where practical.
  Fleet size alone is not the innovation. Measured scalable behaviour is.

## Slide 5
System Architecture
Hybrid by design - central for orchestration, edge for safety
CENTRAL WMS / CLOUD High-level orders, analytics, dashboard
EDGE MESH / COORDINATION NETWORK peer state, path intent, conflicts, auctions, reservations
AMR 1 local agent local plan local coord
AMR 2 local agent local plan local coord
AMR 3 local agent local plan local coord
AMR 4 local agent local plan local coord
AMR N local agent local plan local coord
Movement decisions do NOT round-trip through the central server.
If the central RMS dies: local collision avoidance, conflict resolution, rerouting and failure detection continue. Dashboard and analytics degrade.
We will not claim the central server is irrelevant - it matters for orchestration. We claim the fleet does not freeze without it.

## Slide 6
The Six Modules
Who owns what, and where they meet
 | Member | Owns | Key output consumed by others
M1 | Frontend / UI-UX | 12 screens, canvas map, Decision Inspector | the demo itself
M2 | Backend / INTEGRATION | FastAPI, WebSocket, docker-compose, contracts | fleet snapshot -> M1
M3 | AI / ML | dataset, action model, congestion prediction | MLAdvice -> M4, CongestionField -> M5
M4 | Robotics / Multi-Agent | conflicts, reservations, auctions, deadlock | AuctionDecision, directives -> M5
M5 | Simulation + PLANNING | warehouse, 50 robots, A*, baseline policy | AMRState + MovementIntent -> M4
M6 | Database / Analytics | event store, BENCHMARK HARNESS, KPIs | the headline 20% number
Two changes from the original split, both deliberate:
  A* PATH PLANNING moved to M5 - the planner needs the warehouse grid that M5 already owns. Without a planner there are no paths, so no conflicts, so nothing to coordinate.
  M2 is also INTEGRATION OWNER - six modules that have never run together is the classic way hackathon teams fail. Someone must own the seam, and the API layer is where everything physically meets.

## Slide 7
Honest Starting Position
M4 coordination core is already built, audited and tested
296
tests passing, verified 2026-09-20
~3.1k
lines of production coordination code
4A
phases complete (1, 2, 3, 4A)
0
critical or high audit findings
Module | Lines | Status
auction.py - decentralized auction core | 1003 | COMPLETE + AUDITED
reservation.py - spatio-temporal reservations | 949 | COMPLETE
conflict.py - spatio-temporal conflict detection | 436 | COMPLETE
models.py / messages.py - contracts | 396 | COMPLETE
peer_registry.py / intent_registry.py | 286 | COMPLETE
transport.py - Protocol only, no implementation | 81 | STEP 4B
distributed runtime, deadlock, heartbeat, benchmark | - | NOT STARTED
This is the real baseline. Everything marked NOT STARTED is genuinely not started - no invented progress.

## Slide 8
Four Phases
Ordered to kill risk early, not late
Phase | Goal | Definition of done | Why this order
1 | Skeleton that MOVES | 3 robots, real A*, real conflicts, real auctions, ugly UI, one command boots it | Integration risk dies on day 1, not day 30
2 | MEASUREMENT | Benchmark harness + stop-and-wait baseline + event store = a REAL number | Both SIH success criteria need this. No number, no score
3 | Scale + intelligence | 50 robots, spatial broad phase, ML model, deadlock detection, failure recovery | Now improvements can be measured against Phase 2
4 | Novelty + polish | N1/N2/N3, fault injection, beautiful dashboard, demo rehearsal, Q&A drills | Novelty on a measured system wins. On an unmeasured one it loses
HARD RULE: no novelty features until Phase 2 produces a real measured number. This is the single most important scheduling decision in the plan.

## Slide 9
M1 - Frontend / UI-UX
Your mission and the features you own
Build the operational control centre: the screens that make invisible coordination visible and demo-ready.
Live Warehouse Command Center - map-first view, 50+ robots at 30 fps
Fleet Overview - health, active robots, tasks, failures, KPIs
Robot Detail - state, task, battery, path, decisions, peer context
Decision Inspector - WHY a robot proceeded / waited / rerouted
  including the counterfactual panel (N2): 'R12 would have won if...'
Incident Center - conflicts, deadlocks, failures, blocked aisles
Benchmark Center - baseline vs SWARMOS side by side
Replay - scrub the timeline of an entire run
Simulation Lab - scenario / robot count / fault injection controls

## Slide 10
M1 - Files and Interfaces
What you own on disk, and who you depend on
FILES YOU OWN
frontend/src/screens/* (one file per screen)
frontend/src/map/WarehouseCanvas.tsx (canvas/WebGL renderer)
frontend/src/api/client.ts (REST client, generated types)
frontend/src/api/socket.ts (WebSocket fleet stream)
frontend/src/components/* (shared UI primitives)
YOU CONSUME (inputs from others)
  Fleet snapshot over WebSocket from M2 (~10 Hz); REST for tasks/scenarios/benchmarks; AuctionDecision.utility_breakdown for the Decision Inspector.
YOU PRODUCE (outputs others depend on)
  User actions: create task, start/stop scenario, inject fault, run benchmark, load replay.
STACK
  React 18 + TypeScript + Vite + Tailwind + PixiJS or Konva (map) + Recharts (charts)
All contracts are defined in docs/INTEGRATION_CONTRACTS.md. Change that file first, then your code.

## Slide 11
M1 - Week by Week
Every week ends with something demo-visible
Week | Deliverable
W1 | Static shell, routing, theme, mock-data map with 5 robots
W2 | Live WebSocket wiring, real robot movement on canvas, Fleet Overview
W3 | Decision Inspector + Incident Center on real coordination data
W4 | Benchmark Center + Replay scrubber
W5 | 50-robot performance pass, polish, demo rehearsal
Rules that apply to everyone:
  Nothing is 'done' until it runs in the integrated demo.
  Commit small and often. Never break main.
  If you are blocked for more than half a day, say so immediately.
  No secrets in code, docs, commits or screenshots. Ever.

## Slide 12
M1 - Your Q&A Defence
SIH judges question members individually. Know these cold.
Q: How do you render 50+ robots at 30 fps without React re-rendering everything?
  A: High-frequency map state never enters React state. The socket writes into a mutable ref and the canvas renders from a requestAnimationFrame loop. Only low-frequency aggregates (KPIs, incident counts) are React state.
Q: Is the Decision Inspector generated text?
  A: No. It renders the actual UtilityBreakdown numbers computed by the coordination engine - six weighted components and their sum. No LLM, no prose generation.
Q: What happens to the UI if the backend dies mid-demo?
  A: The socket layer detects disconnect, the UI switches to a DEGRADED banner and keeps showing last-known state instead of blanking. This mirrors the system's own degraded-mode story.
Q: Why dark theme?
  A: It is an industrial command-centre convention - reduces eye strain in control rooms and makes semantic state colours (green/amber/red) read clearly. It is a functional choice, not decoration.
Q: How does a judge verify zero collisions?
  A: The Fleet Overview carries a live collision counter fed from the simulator's own collision check, and the Replay screen lets you re-examine any moment of the run.

## Slide 13
M2 - Backend / Integration Owner
Your mission and the features you own
Own the FastAPI service AND the integration seam: one command must boot the entire demo.
FastAPI service: REST + WebSocket, OpenAPI schema as the contract
WebSocket fleet telemetry fan-out at ~10 Hz
Task / fleet management API (create, assign, track, complete)
Simulation control API: start / pause / step / seed / scenario
Fault injection API: kill robot, block aisle, drop packets, kill RMS
Benchmark orchestration: run baseline + SWARMOS, return comparison
INTEGRATION OWNER: docker-compose, single-command boot, smoke test
OWNER of docs/INTEGRATION_CONTRACTS.md

## Slide 14
M2 - Files and Interfaces
What you own on disk, and who you depend on
FILES YOU OWN
app/api/main.py (FastAPI app factory)
app/api/routes/*.py (robots, tasks, sim, benchmark, replay)
app/api/ws.py (fleet snapshot broadcaster)
app/api/schemas.py (pydantic request/response models)
app/orchestrator.py (drives sim + coordination + persistence)
docker-compose.yml, Makefile, scripts/smoke_test.sh
YOU CONSUME (inputs from others)
  AMRState + tick events from M5; decisions/conflicts from M4; KPIs and replay frames from M6; advisories from M3.
YOU PRODUCE (outputs others depend on)
  Fleet snapshot (WebSocket), REST API for everything, event stream into M6's store.
STACK
  Python 3.11 + FastAPI + Uvicorn + Pydantic v2 (already in pyproject.toml). Docker Compose for the demo.
All contracts are defined in docs/INTEGRATION_CONTRACTS.md. Change that file first, then your code.

## Slide 15
M2 - Week by Week
Every week ends with something demo-visible
Week | Deliverable
W1 | App skeleton, /health, robot list from a stub sim, OpenAPI live
W2 | Real orchestrator loop: sim tick -> coordination -> snapshot -> WS
W3 | Task API + simulation control + fault injection endpoints
W4 | Benchmark orchestration endpoint + replay endpoints
W5 | docker-compose one-command boot, smoke test, hardening
Rules that apply to everyone:
  Nothing is 'done' until it runs in the integrated demo.
  Commit small and often. Never break main.
  If you are blocked for more than half a day, say so immediately.
  No secrets in code, docs, commits or screenshots. Ever.

## Slide 16
M2 - Your Q&A Defence
SIH judges question members individually. Know these cold.
Q: You call this decentralized, but you have a central FastAPI server. Explain.
  A: The architecture is deliberately hybrid. FastAPI serves orchestration, monitoring and analytics. Time-critical collision avoidance runs in the coordination engine instances, which do not require the server. We demonstrate this by killing the RMS mid-run while the fleet keeps coordinating.
Q: How do six modules stay compatible?
  A: One document, docs/INTEGRATION_CONTRACTS.md, defines every interface, plus the FastAPI OpenAPI schema is generated from Pydantic models so the frontend types cannot drift silently.
Q: How do you push 50 robots at 10 Hz without saturating the socket?
  A: The snapshot is diff-friendly and capped: full state on connect, then per-tick payloads. If a client lags we drop intermediate frames rather than queue them - freshness beats completeness for a live map.
Q: What is your single point of failure?
  A: The orchestrator process, for the dashboard path only. Coordination decisions are computed by the engine instances. We state this limit openly rather than claiming full decentralisation.
Q: How long does it take to start your whole system from scratch?
  A: One command: docker-compose up. There is a smoke test that boots it, runs 3 robots for 30 ticks and asserts zero collisions.

## Slide 17
M3 - AI / ML
Your mission and the features you own
Provide predictive intelligence that is trained on our own simulation data, is measurable, and is advisory - never safety-critical.
Dataset generated from OUR simulator (no external dataset needed)
Feature engineering: local robot density, reservation pressure,
  battery, deadline slack, corridor congestion, historical wait
Action classifier: MOVE / WAIT / REROUTE / CHARGE with confidence
N4 PREDICTIVE CONGESTION FIELD - predict cell occupancy at t+delta
  and feed it to the planner as edge-cost multipliers
Model card: accuracy, confusion matrix, feature importance, limits
Utility weight sensitivity study (answers 'why 0.30?')
A/B harness: reactive coordination vs congestion-aware routing

## Slide 18
M3 - Files and Interfaces
What you own on disk, and who you depend on
FILES YOU OWN
ml/dataset/build_dataset.py (simulator logs -> training table)
ml/features.py (feature extraction, shared at infer)
ml/train_action_model.py (train + evaluate + save)
ml/congestion_field.py (EWMA baseline, then learned model)
ml/serve.py (load model, MLAdvice at inference)
ml/model_card.md (honest metrics and limitations)
YOU CONSUME (inputs from others)
  Event log / dataset export from M6; live AMRState + reservation pressure from M4 at inference time.
YOU PRODUCE (outputs others depend on)
  MLAdvice (advisory action + confidence + features_used) to M4; CongestionField (cost multipliers) to M5's planner.
STACK
  Python 3.11 + scikit-learn (GradientBoosting / RandomForest) + Pandas + NumPy. Start with EWMA, add the learned model after.
All contracts are defined in docs/INTEGRATION_CONTRACTS.md. Change that file first, then your code.

## Slide 19
M3 - Week by Week
Every week ends with something demo-visible
Week | Deliverable
W1 | Define features; get the simulator emitting a labelled event log
W2 | EWMA congestion field working end-to-end into the planner
W3 | Train + evaluate the action classifier, write the model card
W4 | Learned congestion prediction; A/B measured against EWMA
W5 | Weight sensitivity study; Decision Inspector feature display
Rules that apply to everyone:
  Nothing is 'done' until it runs in the integrated demo.
  Commit small and often. Never break main.
  If you are blocked for more than half a day, say so immediately.
  No secrets in code, docs, commits or screenshots. Ever.

## Slide 20
M3 - Your Q&A Defence
SIH judges question members individually. Know these cold.
Q: Where is the AI, really? Is it decoration?
  A: Two concrete places. (1) A congestion predictor that changes planner edge costs, measurably reducing completion time in an A/B test with identical seeds. (2) An action classifier advising MOVE/WAIT/REROUTE/CHARGE. Both are trained on data our simulator generated, and both have reported metrics.
Q: What if your model is wrong? Can it cause a collision?
  A: No, by construction. The model is advisory. Safety is enforced by the deterministic spatio-temporal reservation engine, which the model cannot override. A wrong prediction costs efficiency, never safety.
Q: Why not deep learning / reinforcement learning?
  A: Our dataset is tabular and modest, so gradient boosting is the appropriate choice and is interpretable via feature importance. RL would not converge in the available time and could not be safety-argued. We chose the honest tool, not the impressive-sounding one.
Q: Where did your training data come from?
  A: Our own seeded simulator. Every run is reproducible from its seed, so the dataset is regenerable and auditable - which is stronger than an unrelated downloaded dataset.
Q: Why are the utility weights 0.30 / 0.25 / 0.15 / 0.15 / 0.10 / 0.05?
  A: They started as engineering defaults. We then ran a sensitivity sweep over many weight vectors on identical scenarios and report the region where outcomes are stable. So the numbers are empirically supported, not asserted.

## Slide 21
M4 - Robotics / Multi-Agent Coordination (Adithya)
Your mission and the features you own
Make many robots share contested space safely and efficiently without a central brain making every movement decision.
DONE Steps 1-4A: contracts, peer/intent registries, conflict
  detection, spatio-temporal reservations, auction core - 296 tests
Step 4B: distributed runtime bid exchange over a real transport
  with timeouts, quorum, late bids, re-auction, TTL cleanup
Deadlock detection (distributed wait-for graph + cycle detection)
Deadlock recovery with aging-based anti-starvation guarantee
Heartbeat failure detection + reservation invalidation
WAIT / YIELD / SLOW / REROUTE policy (currently PROCEED/WAIT/YIELD)
N1 VERIFIABLE BIDS - detect a robot lying about its own state
N3 TAMPER-EVIDENT DECISION CHAIN - hash-linked audit trail
N5 Degraded-mode ladder: FULL_MESH / LOCAL / CONSERVATIVE / SAFE_HALT
Spatial broad phase to fix O(N^2) conflict detection
Fault injection: loss, delay, duplication, partition, robot death

## Slide 22
M4 - Files and Interfaces
What you own on disk, and who you depend on
FILES YOU OWN
app/coordination/auction.py 1003 lines (Step 4A, DONE)
app/coordination/reservation.py 949 lines (Step 3, DONE)
app/coordination/conflict.py 436 lines (Step 2, DONE)
app/coordination/models.py 207 lines (Step 1, DONE)
app/coordination/messages.py 189 lines (Step 1, DONE)
app/coordination/peer_registry.py 162 lines (DONE)
app/coordination/intent_registry.py 124 lines (DONE)
app/coordination/transport.py 81 lines (Protocol only)
NEW 4B: auction_runtime.py, inmemory_transport.py, dedup.py,
auction_messages.py, deadlock.py, heartbeat.py
YOU CONSUME (inputs from others)
  AMRState + MovementIntent from M5; MLAdvice from M3.
YOU PRODUCE (outputs others depend on)
  ConflictResult, AuctionDecision (with UtilityBreakdown), reservation state, CoordinationDirective to M5, RerouteRequest to M5's planner, events to M6.
STACK
  Python 3.11 + Pydantic v2 + pytest. No networking deps in the core - transport is injected via a Protocol.
All contracts are defined in docs/INTEGRATION_CONTRACTS.md. Change that file first, then your code.

## Slide 23
M4 - Week by Week
Every week ends with something demo-visible
Week | Deliverable
W1 | Step 4B: transport, dedup, runtime loop, timeouts, TTL, re-auction
W2 | 3-robot vertical slice with M5; spatial broad phase
W3 | Deadlock detection + recovery; heartbeat + reservation invalidation
W4 | N1 verifiable bids; SLOW/REROUTE policy; degraded-mode ladder
W5 | N3 decision chain; fault-injection scenarios; 50-robot scale test
Rules that apply to everyone:
  Nothing is 'done' until it runs in the integrated demo.
  Commit small and often. Never break main.
  If you are blocked for more than half a day, say so immediately.
  No secrets in code, docs, commits or screenshots. Ever.

## Slide 24
M4 - Your Q&A Defence
SIH judges question members individually. Know these cold.
Q: This runs in one process. In what sense is it decentralized?
  A: The winner-selection function compute_ranking is pure and has no shared state. We run N independent engine instances, partition the message bus so they cannot talk, and show every instance independently computes the identical decision_id. That is the convergence property, demonstrated rather than asserted.
Q: How do you guarantee zero collisions?
  A: We do not claim a formal guarantee - that would need proof we have not done. We claim zero collisions in all tested scenarios, enforced by a reservation engine that is the single authority for entering a contested corridor, plus a SAFE_HALT fallback when a robot cannot confirm a reservation.
Q: What stops the same robot losing every auction forever?
  A: An exponential aging term: aging = 1 - exp(-t*ln2/half_life), half_life 60 s. It is bounded, monotonic and weighted at 0.15, so a repeatedly-losing robot's utility rises until it wins. Aging is also the second tie-break key.
Q: Why an auction instead of fixed priorities or a central planner?
  A: Fixed priorities starve low-priority robots and ignore context. A central planner reintroduces the latency and single-point-of-failure the problem statement asks us to avoid. An auction uses local information only, and determinism gives us reproducibility without a central auctioneer.
Q: What if a robot lies about its battery to win?
  A: We cross-check every declared bid value against independently observed peer state. Inconsistent bids are rejected and lower the robot's trust score. We demo this live by making a robot lie.
Q: What are the known limits of your design?
  A: Reservation authority is currently a shared instance, which is a hidden centralised component. Utility weights are empirically tuned, not optimal. We have no formal deadlock-freedom proof. We state all three openly.

## Slide 25
M5 - Simulation + Path Planning
Your mission and the features you own
Own the virtual warehouse, robot motion, AND path planning - plus the stop-and-wait baseline we are measured against.
Warehouse world: grid, racks, aisles, pick stations, charger bays
Robot kinematics for 50 robots (100+ for stress tests)
A* path planning + D* Lite style replanning on blockage
Congestion-aware costs from M3's CongestionField
Scenario scripting: congestion, blocked aisle, robot failure, comms
SEEDED DETERMINISM - same seed reproduces the run exactly
Collision detection (ground truth for the zero-collision claim)
STOP-AND-WAIT BASELINE POLICY - what the 20% is measured against
Tick loop driving the whole simulation

## Slide 26
M5 - Files and Interfaces
What you own on disk, and who you depend on
FILES YOU OWN
sim/world.py (grid, racks, aisles, chargers)
sim/robot.py (kinematics, battery drain, status FSM)
sim/engine.py (tick loop, seeded RNG, collision check)
sim/scenarios.py (named reproducible scenarios)
planner/astar.py (A* on the warehouse grid)
planner/replan.py (D* Lite style incremental replanning)
planner/baseline.py (STOP_AND_WAIT policy)
YOU CONSUME (inputs from others)
  CoordinationDirective + RerouteRequest from M4; CongestionField from M3; scenario commands from M2.
YOU PRODUCE (outputs others depend on)
  AMRState per robot per tick; MovementIntent with a strictly increasing path_version on every replan; collision and task completion events.
STACK
  Python 3.11 + NumPy. Deterministic seeded RNG only - no unseeded randomness anywhere.
All contracts are defined in docs/INTEGRATION_CONTRACTS.md. Change that file first, then your code.

## Slide 27
M5 - Week by Week
Every week ends with something demo-visible
Week | Deliverable
W1 | Grid world + 3 robots moving + A* + seeded tick loop
W2 | Integrate with M4 coordination: directives actually change motion
W3 | Replanning, blocked aisle, robot failure, charger bays
W4 | STOP_AND_WAIT baseline policy + scenario library
W5 | Scale to 50, then 100-robot stress test, performance profiling
Rules that apply to everyone:
  Nothing is 'done' until it runs in the integrated demo.
  Commit small and often. Never break main.
  If you are blocked for more than half a day, say so immediately.
  No secrets in code, docs, commits or screenshots. Ever.

## Slide 28
M5 - Your Q&A Defence
SIH judges question members individually. Know these cold.
Q: Is your simulation physically realistic?
  A: It is a kinematic simulation with velocity limits and battery drain, not a dynamics or sensor simulation. We state that clearly. It is sufficient and appropriate for evaluating coordination behaviour, which is what the problem statement targets.
Q: Why A* and not RRT or a learned planner?
  A: The warehouse is a static discrete grid, where A* is optimal and fast with an admissible heuristic. RRT targets continuous high-dimensional spaces we do not have. For replanning we use a D* Lite style incremental update to avoid full recomputation.
Q: How is path_version handled?
  A: Every replan strictly increments it. This is what lets coordination reject stale bids and stale intents. It is enforced in the planner, not left to callers.
Q: Is the stop-and-wait baseline a fair comparison?
  A: Yes - identical map, identical seed, identical task stream, identical robot count, identical kinematics. The ONLY difference is the coordination policy. Anything else would invalidate the comparison.
Q: Can you reproduce a specific run a judge saw?
  A: Yes. Every run is fully determined by its seed and scenario ID. Same seed, same run, every time - which is also how we generate the ML training data.

## Slide 29
M6 - Database / Analytics + Benchmark
Your mission and the features you own
Own the evidence. Store every event, compute every metric, and produce the headline number the whole submission rests on.
Schema: robots, tasks, events, decisions, conflicts, reservations
Event store with run_id + tick ordering (enables replay)
BENCHMARK HARNESS - the single most important deliverable:
  run STOP_AND_WAIT and SWARMOS on identical seeds, compare
All 10 metrics: completion time, collisions, deadlocks, throughput,
  avg wait, reroutes, distance, congestion, recovery time, comms
KPI aggregation for the dashboard
Replay frame API (reconstruct any tick of any run)
Dataset export for M3's training
Reproducibility: every reported number traceable to a run_id

## Slide 30
M6 - Files and Interfaces
What you own on disk, and who you depend on
FILES YOU OWN
db/schema.sql (tables + indexes)
db/store.py (event write path, batched)
db/queries.py (KPI + replay queries)
benchmark/harness.py (run pairs of policies over seed sets)
benchmark/metrics.py (the 10 metric computations)
benchmark/report.py (comparison table + chart data)
YOU CONSUME (inputs from others)
  Event log from M4 and M5 via M2's orchestrator.
YOU PRODUCE (outputs others depend on)
  KPIs and benchmark comparison for M1 via M2; replay frames; training dataset for M3.
STACK
  SQLite for the demo (zero setup, file-based, replayable), with a Postgres-compatible schema. Pandas for aggregation.
All contracts are defined in docs/INTEGRATION_CONTRACTS.md. Change that file first, then your code.

## Slide 31
M6 - Week by Week
Every week ends with something demo-visible
Week | Deliverable
W1 | Schema + event write path + basic queries
W2 | KPI aggregation feeding the dashboard
W3 | BENCHMARK HARNESS producing the first real comparison number
W4 | All 10 metrics + replay frame reconstruction
W5 | Multi-seed statistical runs (mean + spread, not one lucky run)
Rules that apply to everyone:
  Nothing is 'done' until it runs in the integrated demo.
  Commit small and often. Never break main.
  If you are blocked for more than half a day, say so immediately.
  No secrets in code, docs, commits or screenshots. Ever.

## Slide 32
M6 - Your Q&A Defence
SIH judges question members individually. Know these cold.
Q: Where does the 20% improvement number come from?
  A: From benchmark/harness.py at runtime. It runs both policies over identical seeds and computes the delta in total completion time. It is never hard-coded. We report the seed set and the spread, not a single best run.
Q: How do we know you did not pick a favourable seed?
  A: We run a set of seeds and report mean and spread. Every number is traceable to a run_id in the database, and any run can be replayed.
Q: Why SQLite and not something bigger?
  A: The demo must boot with zero setup and be replayable from a single file. The schema is Postgres-compatible, so scaling is a configuration change, not a redesign. Choosing the smallest thing that works is an engineering decision.
Q: Can you prove zero collisions rather than assert it?
  A: The simulator performs an independent geometric collision check every tick and writes a COLLISION event. Zero collisions means zero such rows, and that query is run live in the demo.
Q: What is the write load at 50 robots?
  A: Events are batched per tick rather than written individually, and the event table is indexed on (run_id, tick). Persistence is off the simulation's critical path.

## Slide 33
Four Novelty Features
One coherent story, told four ways
 | Feature | Owner | The 30-second stage moment
N1 | Verifiable bids / anti-cheat coordination | M4 | 'I'll make R17 lie about its battery' - it is flagged, loses, fleet runs on
N2 | Counterfactual Decision Inspector | M1 + M4 | 'R12 lost by 0.03 - it would have won with 14s more waiting time'
N3 | Tamper-evident decision chain | M4 + M6 | Re-run the seed: identical hash. Corrupt one record: verification points at it
N4 | Predictive congestion field | M3 + M5 | A/B same seed: congestion-aware routing measurably finishes faster
The narrative that ties them together:
  SWARMOS makes coordination decisions that are PREDICTIVE (N4), EXPLAINABLE (N2), VERIFIABLE even when a robot lies (N1), and REPRODUCIBLE and AUDITABLE after the fact (N3).
Why these four: each builds on determinism and explainability work that is ALREADY DONE - cheap for us, expensive for anyone else to copy. None requires a new technology, so we stay clear of technology soup.
Deliberately NOT doing: blockchain buzzwords, RL for yield policy, forced ROS2/Zenoh, deep learning for appearance, formal certification claims.

## Slide 34
The 8-Minute Demo Script
Rehearsed, timed, with a fallback
Min | What the judge sees | Driver
0:00 | 50 AMRs operating normally on the command centre map | M1
1:00 | Create overlapping-path congestion; future conflicts light up | M1
2:00 | Open the auction: utility breakdown, winner, reservation | M4
3:00 | Winner proceeds, loser waits/yields/reroutes - live on the map | M4
3:45 | Decision Inspector counterfactual: why R12 lost, by how much | M1
4:30 | Block an aisle: affected robots invalidate paths and reroute | M5
5:15 | Kill R27: heartbeat timeout, reservations invalidated, task recovered | M4
6:00 | Make a robot LIE about its battery: bid rejected, trust drops | M4
6:45 | Kill the central RMS: local coordination continues | M2
7:15 | Benchmark Center: measured comparison vs stop-and-wait | M6
7:45 | Replay the same seed: identical decision hash | M6
FALLBACK, non-negotiable: a pre-recorded video AND a seeded replay file on a USB stick. Venue Wi-Fi and live demos fail. Never present without a fallback.

## Slide 35
Engineering Charter
The rules we hold each other to
NO fake AI, fake metrics, fake distributed behaviour or decorative features.
NO hard-coded benchmark results. The number comes from the harness or it does not exist.
NO unsupported claims: no formal safety certification, no proven optimality, no guaranteed deadlock freedom. We say 'in all tested scenarios'.
NO secrets in source, docs, commits, logs or screenshots.
NO giant files without a strong reason. No technology soup.
Do not randomly rewrite another member's working module.
Do not break a contract without a migration note and updated tests.
Run the tests after every change. Inspect the diff before committing.
Acknowledged limitations we will state OPENLY to judges:
  Reservation authority is currently a shared instance - a hidden centralised component.
  Utility weights are empirically tuned, not proven optimal.
  Simulation is kinematic, not full dynamics or sensor simulation.
  No formal deadlock-freedom proof.
Judges reward acknowledged limitations. They punish limitations they discover themselves.

## Slide 36
What I Need From You This Week
Then we lock the architecture and build
1. Read this deck and push back hard. If your section is wrong, say so.
2. Send me your status document using the prompt in docs/TEAM_MEMBER_STATUS_PROMPT.md
  Be honest about what is NOT built. Guessing is worse than 'not started'.
  Section 5 (data contracts) matters most - it is where integration breaks.
  Do NOT paste any tokens, keys or passwords into the output.
3. First team call agenda - we must decide these together:
  Coordinate system: continuous metres vs grid cells, and who converts
  Robot ID and task ID naming format
  Who is authoritative for robot state (proposal: M5's simulator)
  Tick rate, and who drives the loop
  Confirmation that ML is ADVISORY, never in the safety path
4. Then: I finish Step 4B, M5 gets 3 robots moving, and we do the vertical slice together.
Deck version v1. It becomes v2 once your real status documents are in - this version contains my assumptions about your modules.